## Slide 2: Wind turbine control basics
Wind Turbine Control Online Course
Alan Wai Hou Lio
Researcher, DTU Wind Energy
wali@dtu.dk

## Slide 3: Lecturers
Alan Wai Hou Lio
Researcher, DTU Wind Energy
wali@dtu.dk
Day 1, 2 and 3
Anca Daniela Hansen
Associate Professor, DTU Wind Energy
anca@dtu.dk
Day 4

## Slide 4: Nergica introduction
Background
What do you do daily in your work?
Why are you interested in this course?

## Slide 5: Course structure
Day 1
8:00-9:15 Lecture 1: Wind turbine control basics:
9:30-10:45 Lecture 2: Controller design and tuning: Region 2 (Below-rated region)
10:45-11:00 Introduction to mini-project and Matlab turbine model
Day 2
8:00-9:15 Lecture 3: Controller design and tuning: Region 2.5 and 3 (transition and above-rated region)
9:30-10:45 Q&A on mini-project
Day 3
8:00-9:15 Lecture 4: Introduction to Supervisory control, advanced control topics and DTU Wind Energy Controller
9:30-10:45 Mini-project presentations
Day 4
8:00-10:00 Lecture 5: Introduction to electrical control concepts
Day 1
8:00-9:15 Lecture 1: Wind turbine control basics:
9:30-10:45 Lecture 2: Controller design and tuning: Region 2 (Below-rated region)
10:45-11:00 Introduction to mini-project and Matlab turbine model
Day 2
8:00-9:15 Lecture 3: Controller design and tuning: Region 2.5 and 3 (transition and above-rated region)
9:30-10:45 Q&A on mini-project
Day 3
8:00-9:15 Lecture 4: Introduction to Supervisory control, advanced control topics and DTU Wind Energy Controller
9:30-10:45 Q&A on mini-project
Day 4
8:00-10:00 Lecture 5: Introduction to electrical control concepts
10:15-11:00 Mini-project presentations
New
Old

## Slide 6: Learning objectives
After this session you should be able to:
List and explain the controllers used in wind turbines
Explain the control objective of each control region
Understand the Proportional-Integral (PI) controller

## Slide 7: Basic control concepts
What is control? What does it mean to control a system?
System
Inputs
Outputs
Disturbance
Temperature
(output)
Valve
(Input)
Sun
(disturbance)
Speed
(output)
Accelerator
(input)
Wind/other cars
(disturbance)
The actions that could
influence the output
The expected behaviour
of the system
Wind turbine
Inputs
??
Outputs
??
Disturbance ??
Think

## Slide 8: Let’s control a wind turbine
System
Inputs
Outputs
Disturbance
pitch, Gen. torque,
Yaw angle
wind
power, rotor speed
Three required controllers:
Blade pitch controller
Generator torque controller
Yaw controller
Pitch angle
Generator torque
Power
Wind
Yaw angle
Rotor speed
?

## Slide 9: Wind turbine control objectives
Region 2.5
Objectives: (1) Optimize power production at below rated wind speeds
(2) Limit power and loads at above rated wind speeds
Region 2
Below rated
Region 3
Above rated
Pitch control
Torque control
Rated wsp
Regions:
Variable speed, optimal power tracking
Rotor speed regulation
Power and speed regulation

## Slide 10: Open-loop control
What is it?
Outputs
Wind
Control Inputs
Temperature
Valve
(without thermostat)
Sun
(disturbance)
In short…the output has no effect on the input

## Slide 11: Open-loop Example: Part_1.m
DTU 10 MW
  Rated power = 10MW
  Rated Rotor Speed = 1.005 rad/s
  Wind Speed: Steady 13 m/s, above-rated
Desired Outputs
Tip:
Power = Rotor Speed * Torque
Exercise: Open-loop controller
Open part_1.m
Change the value for OpenLoop_Torque and OpenLoop_Pitch so that the rotor speed and generated power are regulated to the desired outputs.

## Slide 12: Open-loop Example: Part_1.m
inputs:
Pitch angle: 6.78 deg
Generator torque: 10e6/1.005 Nm
Desired Outputs

## Slide 13: Open-loop Example: Part_1.m
Now, the wind speed (disturbance) increases from 13 m/s to 14 m/s
What will happen to the rotor speed and power?
Change the simulation time to 300 s
Exercise: Open-loop controller 2
Change simulation time to 300 and see what happens

## Slide 14: Open-loop Example: Part_1.m
When the simulation length is increased to 300s
Wind speed changed
Control inputs need to be changed in real-time
Desired Outputs
inputs:
Pitch angle: 6.78 deg
Generator torque: 10e6/1.005 Nm

## Slide 15: Closed-loop control
Inputs
Outputs
Wind
Before (OL):
Now (CL):
error
C
Set Point

## Slide 16: Let’s consider Region 3 control for now
Ensures correct power
Controller! (Need to define)
Region 3
Above rated

## Slide 17: Proportional (P) controller: Part_2.m
Exercise: Proportional controller
Open part_2.m
Change the value for Kp3 so that the rotor speed and generated power converge to the desired outputs.
Change the simulation to 400 seconds.
Desired Outputs

## Slide 18: Proportional (P) controller
Kp alone cannot make the rotor speed to converge
Change in disturbance
“Offset error”  P-controller inadequate

## Slide 19
19
Proportional-Integral (PI) pitch controller: part_2.m
Exercise: PI controller
Open part_2.m
Change the values for Kp3 and Ki3 so that the rotor speed and generated power converge to the desired outputs
Change the simulation to 400 seconds. What do you see?
Desired Outputs

## Slide 20
Rotor speed is regulated!
Power is regulated!
Proportional-Integral (PI) pitch controller
Controller (Need to designed)
Results: Kp = 10.8, Ki = 2.2

## Slide 21: How about the derivative (D) term?
Not commonly used in wind turbine control
Derivative of the measurement typically contains noises
Filtered rotor speed measurement from V52 and its derivative

## Slide 22: Summary
In an open-loop system, the controller does not use the knowledge of the system measurement
Closed-loop controller regulates the system (wind turbine) based on the feedback mechanism.
  The system input is in response to the system measurement
Proportional controller alone cannot regulate the system to the desired output without an offset
Proportional-Integral (PI) controller can successfully regulate the system and minimise any offset between the desired output and system measurement.